## Slide 1: 补充材料-2 Operations Strategy & Competitiveness (Ii)

## Slide 2: What you should learn
Just-In-Time (JIT)
Value Stream Mapping (VSM) for lean manufacturing
Theory of Constraints (TOC)

## Slide 3: What you should learn
Just-In-Time (JIT)
Value Stream Mapping (VSM) for lean manufacturing
Theory of Constraints (TOC)

## Slide 4: JIT/Lean Operations
Good production systems require that managers address three issues that are pervasive and fundamental to operations management: eliminate waste, remove variability, and improve throughput

## Slide 5: 1. Eliminate Waste
Waste is anything that does not add value from the customer point of view
Storage, inspection, delay, waiting in queues, and defective products do not add value and are 100% waste

## Slide 6: Ohno’s Seven Wastes
Overproduction
Queues
Transportation
Inventory
Motion
Overprocessing
Defective products

## Slide 7: Eliminate Waste
Other resources such as energy, water, and air are often wasted
Efficient, sustainable production minimizes inputs, reduces waste
Traditional “housekeeping” has been expanded to the 5 Ss

## Slide 8: The 5 Ss
Sort/segregate – when in doubt, throw it out
Simplify/straighten – methods analysis tools
Shine/sweep – clean daily
Standardize – remove variations from processes
Sustain/self-discipline – review work and recognize progress

## Slide 9: The 5 Ss
Sort/segregate – when in doubt, throw it out
Simplify/straighten – methods analysis tools
Shine/sweep – clean daily
Standardize – remove variations from processes
Sustain/self-discipline – review work and recognize progress
Two additional Ss
Safety – build in good practices
Support/maintenance – reduce variability and unplanned downtime

## Slide 10: 2. Remove Variability
JIT systems require managers to reduce variability caused by both internal and external factors
Variability is any deviation from the optimum process
Inventory hides variability
Less variability results in less waste

## Slide 11: Sources of Variability
Incomplete or inaccurate drawings or specifications
Poor production processes resulting in incorrect quantities, late, or non-conforming units
Unknown customer demands

## Slide 12: Sources of Variability
Incomplete or inaccurate drawings or specifications
Poor production processes resulting in incorrect quantities, late, or non-conforming units
Unknown customer demands
Both JIT and inventory reduction are effective tools in identifying causes of variability

## Slide 13: 3. Improve Throughput
The time it takes to move an order from receipt to delivery
The time between the arrival of raw materials and the shipping of the finished order is called manufacturing cycle time
A pull system increases throughput

## Slide 14: Improve Throughput
By pulling material in small lots, inventory cushions are removed, exposing problems and emphasizing continual improvement
Manufacturing cycle time is reduced
Push systems dump orders on the downstream stations regardless of the need

## Slide 15: Just-In-Time (JIT)
Powerful strategy for improving operations
Materials arrive where they are needed when they are needed
Identifying problems and driving out waste reduces costs and variability and improves throughput
Requires a meaningful buyer-supplier relationship

## Slide 16: JIT and Competitive Advantage

## Slide 17
JIT and Competitive Advantage

## Slide 18: JIT Partnerships
JIT partnerships exist when a supplier and purchaser work together to remove waste and drive down costs
Four goals of JIT partnerships are:
  Removal of unnecessary activities
  Removal of in-plant inventory
  Removal of in-transit inventory
  Improved quality and reliability

## Slide 19: JIT Partnerships

## Slide 20: JIT Layout
Reduce waste due to movement
JIT Layout Tactics
Build work cells for families of products
Include a large number operations in a small area
Minimize distance
Design little space for inventory
Improve employee communication
Use poka-yoke (fail safe) devices
Build flexible or movable equipment
Cross-train workers to add flexibility

## Slide 21: Process layouts

## Slide 22: Group technology layout

## Slide 23: Distance Reduction
Large lots and long production lines with single-purpose machinery are being replaced by smaller flexible cells
Often U-shaped for shorter paths and improved communication
Often using group technology concepts

## Slide 24: Increased Flexibility
Cells designed to be rearranged as volume or designs change
Applicable in office environments as well as production settings
Facilitates both product and process improvement

## Slide 25: Impact on Employees
Employees may be cross trained for flexibility and efficiency
Improved communications facilitate the passing on of important information about the process
With little or no inventory buffer, getting it right the first time is critical

## Slide 26: Reduced Space and Inventory
With reduced space, inventory must be in very small lots
Units are always moving because there is no storage

## Slide 27: JIT Inventory
Inventory is at the minimum level necessary to keep operations running
JIT Inventory Tactics
Use a pull system to move inventory
Reduce lot sizes
Develop just-in-time delivery systems with suppliers
Deliver directly to point of use
Perform to schedule
Reduce setup time
Use group technology

## Slide 28: Reduce Variability
Inventory level
Process downtime
Scrap
Setup time
Late deliveries
Quality problems

## Slide 29: Reduce Variability
Inventory level
Process downtime
Scrap
Setup time
Late deliveries
Quality problems

## Slide 30: Reduce Variability
Inventory level
Process downtime removed
No scrap
Setup time reduced
Late deliveries
Quality problems removed

## Slide 31: Reduce Inventory
Reducing inventory uncovers the “rocks”
Problems are exposed
Ultimately there will be virtually no inventory and no problems
Shingo says “Inventory is evil”

## Slide 32: Reduce Lot Sizes
200 –
100 –
Inventory
Time
Q2 When average order size = 100
average inventory is 50
Q1 When average order size = 200
average inventory is 100

## Slide 33: Reduce Lot Sizes
Ideal situation is to have lot sizes of one pulled from one process to the next
Often not feasible
Can use EOQ analysis to calculate desired setup time
Two key changes necessary
  Improve material handling
  Reduce setup time

## Slide 34: Reduce Setup Costs
High setup costs encourage large lot sizes
Reducing setup costs reduces lot size and reduces average inventory
Setup time can be reduced through preparation prior to shutdown and changeover

## Slide 35: Lower Setup Costs
Sum of ordering and holding costs
Holding cost
Setup cost curves (S1, S2)
T1
S1
T2
S2
Cost
Lot size

## Slide 36: Reduce Setup Times
Use one-touch system to eliminate adjustments (save 10 minutes)
Step 4
Step 5
Training operators and standardizing work procedures (save 2 minutes)
Initial Setup Time
Step 2
Move material closer and improve material handling (save 20 minutes)
Step 1
Separate setup into preparation and actual setup, doing as much as possible while the machine/process is operating
(save 30 minutes)
Step 3
Standardize and improve tooling (save 15 minutes)
90 min —
60 min —
45 min —
25 min —
15 min —
13 min —
—
Repeat cycle until subminute setup is achieved
Step 6
Single Minute Exchange of Dies (SMED)

## Slide 37: JIT Scheduling
Schedules must be communicated inside and outside the organization
Level schedules
  Process frequent small batches
  Freezing the schedule helps stability
Kanban
  Signals used in a pull system

## Slide 38: JIT Scheduling
Better scheduling improves performance
JIT Scheduling Tactics
Communicate schedules to suppliers
Make level schedules
Freeze part of the schedule
Perform to schedule
Seek one-piece-make and one-piece move
Eliminate waste
Produce in small lots
Use kanbans
Make each operation produce a perfect part

## Slide 39: Level Schedules
Process frequent small batches rather than a few large batches
Make and move small lots so the level schedule is economical
“Jelly bean” scheduling
Freezing the schedule closest to the due dates can improve performance

## Slide 40: Scheduling Small Lots
A
B
C
A
A
A
B
B
B
B
B
C
JIT Level Material-Use Approach
A
C
A
A
A
B
B
B
B
B
C
C
B
B
B
B
A
A
Large-Lot Approach
Time

## Slide 41: Kanban
Kanban is the Japanese word for card
The card is an authorization for the next container of material to be produced
A sequence of kanbans pulls material through the process
Many different sorts of signals are used, but the system is still called a kanban

## Slide 42: Kanban
User removes a standard sized container
Signal is seen by the producing department as authorization to replenish
Part numbers mark location
Signal marker on boxes

## Slide 43: Kanban
Kanban
Kanban
Final assembly
Work cell
Kanban
Material/Parts Supplier
Finished goods
Customer order

## Slide 44: JIT Quality
Strong relationship
  JIT cuts the cost of obtaining good quality because JIT exposes poor quality
  Because lead times are shorter, quality problems are exposed sooner
  Better quality means fewer buffers and allows simpler JIT systems to be used

## Slide 45: JIT Quality Tactics
Use statistical process control
Empower employees
Build fail-safe methods (poka-yoke, checklists, etc.)
Expose poor quality with small lot JIT
Provide immediate feedback

## Slide 46: JIT in Services
The JIT techniques used in manufacturing are used in services
  Suppliers
  Layouts
  Inventory
  Scheduling

## Slide 47: What you should learn
Just-In-Time (JIT)
Value Stream Mapping (VSM) for lean manufacturing
Theory of Constraints (TOC)

## Slide 48: Lean Manufacturing
"Lean," is a production practice that considers the expenditure of resources for any goal other than the creation of value for the end customer to be wasteful, and thus a target for elimination.
---- John Krafcik (1988)

## Slide 49
Obstacle of Traction:
Waste

## Slide 50
What is WASTE?
Any Activity that DOES NOT increase the Market Form or Function of the Product or Service based on the Critical Customer Requirements.
These are things the customer is NOT willing to pay for.

## Slide 51: Definition of Value Added
Value Added
Any activity that increases the market form or function of the product or service. (These are things the customer is willing to pay for.)
Non-Value Added
Any activity that does not add market form or function or is not necessary. (These activities should be eliminated, simplified, reduced, or integrated.)

## Slide 52: Lean = Eliminating the Wastes
Value Added
Typically 95% of all lead time is non-value added
Non-Value Added
Defects
Overproduction
Waiting
Not Utilizing Employees
Transportation
Inventory
Motion
Excess Processing

## Slide 53: Where is the Waste?
Defects – incomplete or incorrect information
Overproduction – releasing work before next process can work on them, unbalanced work loads
Waiting – unbalanced work loads, slow system response, incomplete information, approvals
Not Utilizing Employees – old guard thinking, politics, high turnover, low investment in training
Transportation – poor layout, poor flow
Inventory – large batches, complexity to complete task
Motion – poor organization, no standard work
Excess Processing – excess communication, lack of communication, unnecessary approvals, customer requirements are not clearly understood
All processes have waste.

## Slide 54
Without Change
There Can Be No Improvement
“The definition of insanity is doing the same thing over and over and expecting different results.”
Albert Einstein

## Slide 55: Value Stream mapping
Value Stream Mapping is a tool used to create a material and information flow map of a product or processes. It allows firms to map the flow of products in the back door as raw material, through all manufacturing process steps, and off the loading dock as finished product.

## Slide 56
Identify
waste
Measure
&
Adjust
Current
state
Future
state
Implement
Continuous
Incremental
Improvement
The Lean Process

## Slide 57
Understanding the Process
Information and Material Flow
Data Driven Decision Process
Benefit of Value Stream Mapping

## Slide 58: Lean Operations
Different from JIT in that it is externally focused on the customer
Starts with understanding what the customer wants
Optimize the entire process from the customer’s perspective

## Slide 59
“Whenever there is a product or service for a customer, there is a value stream.
The challenge lies in seeing it.”
Look for Value Streams

## Slide 60: Value Stream Mapping Steps
Select product / service family
Draw Current State map. Understanding how the process currently operates.
Identify opportunities for elimination of waste and areas of improvement to meet customer’s needs.
Draw the Future State map. Design a lean flow using lean techniques.
Develop action plan and implement it.
Product / Service
family
Future state
drawing
drawing
Current state
Plan and
Implementation

## Slide 61: Basic Steps of VSM
Define the boundaries
Define the value
Identify the tasks and flows of material and information between them.
Identify resources for each task and flow
Create the current state map
  Identify value added and waste
  Reconfigure the process to eliminate waste
Visualize the “Ideal State” and create future state map
Develop Action plans and tracking

## Slide 62
Incoming
Orders
Receive Order
Fax
Check Credit
FIN
Review & Enter Order
MRP
Reconcile Order
MRP
Confirm Order
Phone
Finalize Order
MRP
MRP
MRP
Production
Schedule
Semi-Weekly
Ship Schedule
.5 days
.5 days
.2 days
.2 days
.25 days
1 day
½ min
1 min
10 min
1 min
7 min
5 min
Total Lead Time = 2.65 days
Total Processing Time= 24.5 min
Order Entry Process
Current State - Sept. 2007
First Pass Yield = 34.4%
P/T = ½ min
Batch = 4
hours
IN
P/T = 1 min
% Accept = 90%
Batch = 4 hours
IN
P/T = 10 min
% C&A = 60%
Batch = 1.6 hours
IN
P/T = 1 min
%C&A = 75%
Batch = 1.6 hours
IN
P/T =7 min
%C&A = 85%
Batch = 2 hours
IN
P/T = 5 min
Batch = 1day
IN
Weekly Fax
Information
Material
Notes: ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## Slide 63: Future State Questions
What does the customer really need?
How often will we check our performance to customer needs?
Which steps create value and which are waste?
How can we flow work with fewer interruptions?
How do we control work between interruptions? How will work be prioritized?
Is there an opportunity to balance the work load and/or different activities?
What process improvements will be necessary?
Notes: ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## Slide 64
Incoming
Orders
Receive Order
Fax
Check Credit
FIN
Review & Enter Order
MRP
Reconcile Order
MRP
Confirm Order
Phone
Finalize Order
MRP
MRP
MRP
Production
Schedule
Semi-Weekly
Ship Schedule
.5 days
.5 days
.2 days
.2 days
.25 days
1 day
½ min
1 min
10 min
1 min
7 min
5 min
Total Lead Time = 2.65 days
Total Processing Time= 24.5 min
Order Entry Process
Current State - Sept. 2007
First Pass Yield = 34.4%
P/T = ½ min
Batch = 4
hours
IN
P/T = 1 min
% Accept = 90%
Batch = 4 hours
IN
P/T = 10 min
% C&A = 60%
Batch = 1.6 hours
IN
P/T = 1 min
%C&A = 75%
Batch = 1.6 hours
IN
P/T =7 min
%C&A = 85%
Batch = 2 hours
IN
P/T = 5 min
Batch = 1day
IN
Weekly Fax
What does the customer really need?
How often will we check our performance to customer needs?
All orders will be processed within one hour of receipt (6 orders processed each hour).
Each hour.
460 minutes
46 Orders
= 10 minutes/order
Takt Time =
Notes: ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## Slide 65: Takt Time
Takt time:
the available production time divided by customer demand.

## Slide 66
Incoming
Orders
Receive Order
Fax
Check Credit
FIN
Review & Enter Order
MRP
Reconcile Order
MRP
Confirm Order
Phone
Finalize Order
MRP
MRP
MRP
Production
Schedule
Semi-Weekly
Ship Schedule
.5 days
.5 days
.2 days
.2 days
.25 days
1 day
½ min
1 min
10 min
1 min
7 min
5 min
Total Lead Time = 2.65 days
Total Processing Time= 24.5 min
Order Entry Process
Current State - Sept. 2007
First Pass Yield = 34.4%
P/T = ½ min
Batch = 4
hours
IN
P/T = 1 min
% Accept = 90%
Batch = 4 hours
IN
P/T = 10 min
% C&A = 60%
Batch = 1.6 hours
IN
P/T = 1 min
%C&A = 75%
Batch = 1.6 hours
IN
P/T =7 min
%C&A = 85%
Batch = 2 hours
IN
P/T = 5 min
Batch = 1day
IN
Weekly Fax
Stop walking to the FAX that’s waste!!!
Phone
Or WEB
Which steps create value?
Which are waste?
Waste
Over Processing
Waste
Rework
460 minutes
46 Orders
= 10 minutes/order
Takt Time =
Notes: ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## Slide 67
460 minutes
46 Orders
= 10 minutes/order
Takt Time =
Incoming
Orders
Receive Order
Fax
Check Credit
FIN
Review & Enter Order
MRP
Reconcile Order
MRP
Confirm Order
Phone
Finalize Order
MRP
MRP
MRP
Production
Schedule
Semi-Weekly
Ship Schedule
.5 days
.5 days
.2 days
.2 days
.25 days
1 day
½ min
1 min
10 min
1 min
7 min
5 min
Order Entry Process
Current State - Sept. 2007
P/T = ½ min
Batch = 4
hours
IN
P/T = 1 min
% Accept = 90%
Batch = 4 hours
IN
P/T = 10 min
% C&A = 60%
Batch = 1.6 hours
IN
P/T = 1 min
%C&A = 75%
Batch = 1.6 hours
IN
P/T =7 min
%C&A = 85%
Batch = 2 hours
IN
P/T = 5 min
Batch = 1day
IN
Weekly Fax
Finance
Cross Train
Link Finance
/ MRP
On-Line
Order Entry
How can we flow work with fewer interruptions?
Total Lead Time = 1.25 days
Total Processing Time= 11.5 min
NEW METRICS!
First Pass Yield = 90%
Auto
Confirm
Notes: ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## Slide 68
Receive / Credit
Check / Reconcile
Confirm
MRP/FIN
MRP
MRP
Production
Schedule
P/T < 10 min
% accept = 90%
Batch = 1
Order Entry Process
Future State - Sept. 2007
Phone / Web
Semi-Weekly
Ship Schedules
How can we control work between interruptions?
Schedule
Production
via FG Kanban
Implement
Kanban
Kanban will:
Schedule Production to real time demand.
Optimize (level) and Control Inventory.
Link Production to Customer Demand.
Incoming
Orders
Notes: ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## Slide 69
Receive / Credit
Check / Reconcile
Confirm
MRP/FIN
MRP
P/T < 10 min
% accept = 90%
Batch = 1
Order Entry Process
Future State - Sept. 2007
Phone / Web
Semi-Weekly
Ship Schedules
Incoming
Orders
Schedule
Production
via FG Kanban
Shipping
Training
Direct
Schedule
Shipping
If FG Kanban is implemented what improvements can be made to Shipping?
I.T. Link to
Order Entry
Notes: ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## Slide 70
Receive / Credit
Check / Reconcile
Confirm
MRP/FIN
MRP
P/T < 10 min
% accept = 90%
Batch = 1
Order Entry Process
Future State - Sept. 2007
Phone / Web
Incoming
Orders
Schedule
Production
via FG Kanban
Shipping
Total Lead Time < 10 Minutes
Total Processing Time < 10 Minutes
Future State Metrics!
First Pass Yield > 90%
Notes: ________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________________

## Slide 71: Summary:
ALL processes have WASTE that cost you MONEY.
Improvement requires change. To change a process you have to understand the process.
Process Excellence will not be achieved without involving people at all levels of the organization.

## Slide 72: What you should learn
Just-In-Time (JIT)
Value Stream Mapping (VSM) for lean manufacturing
Theory of Constraints (TOC)

## Slide 73: In Practice
How do we measure or evaluate the efficiency or contribution of a person, a machine, or a department of manufacturing system??

## Slide 74: Theory of Constraints
Significance of bottlenecks
  Maximum speed of the process is the speed of the slowest operation
  Any improvements will be wasted unless the bottleneck is relieved
    Bottlenecks must be identified and improved if the process is to be improved

## Slide 75: Theory of Constraints
Purpose is to identify bottlenecks or other constraints and exploit them to the extent possible
  Identification of constraints allows management to take action to alleviate the constraint in the future
    Reduce cycle time
      Time from receipt of customer order to shipment
    Improve manufacturing cycle efficiency (MCE)
      Processing time / total cycle time

## Slide 76: The Need for TOC
Theory of Constraints
  Uses linear programming to determine best use of limited resources
    Indicates what should be produced and in what quantities

## Slide 77: Theory of Constraints
Constraining resource must be maximized
  All other operations must be geared toward this goal
    May require suboptimization in other areas
      Upstream operations must provide only what the constraint can handle
      Downstream operations will only receive what the constraint can put out

## Slide 78: Theory of Constraints
Constraint must be kept operating at its full capacity
  If not, the entire process slows further
Focus is on maximizing throughput
  Sales – totally variable costs
  All other costs treated as fixed operational expenses
    Cannot vary much in the short-run

## Slide 79: Theory of Constraints
Based on the concepts of drum, buffer and ropes
  Drum
    Output of the constraint is the drumbeat
      Sets the tempo for other operations
      Tells upstream operations what to produce
      Tells downstream operations what to expect
  Buffer
    Stockpile of work in process in front of constraint
      Precaution to keep constraint running if upstream operations are interrupted
  Rope
    Sequence of processes prior to and including the constraint
      Want to “pull” the rope at the maximum speed
        Speed of the constraint

## Slide 80: Steps in the TOC Process
Internal
  Process constraints
    Machine time, etc.
  Policy constraints
    No overtime, etc.
External
  Material constraints
    Insufficient materials
  Market constraints
    Insufficient demand
Step 1: Identify the system constraints
How is a constraint identified?

## Slide 81: Steps in the TOC Process
Step2: Decide how to exploit the constraint
  Produce the most profitable product mix
  Want it working at 100%
    How much of a buffer?
      Holding costs
        Including risk, quality costs
      Stock-out costs

## Slide 82: Steps in the TOC Process
Step3: Subordinate everything else to the preceding decision
  Plan production to keep constraint working at 100%
  May need to change performance measures to conform upstream activities to the “rope” speed

## Slide 83: Steps in the TOC Process

## Slide 84: Steps in the TOC Process

## Slide 85: Steps in the TOC Process
Step 4: Alleviate the constraint
  Determine how to increase its capacity
Step 5: Repeat the process
  Always a new constraint

## Slide 86: Evaluation of TOC
Advantages
  Improves capacity decisions in the short-run
  Avoids build up of inventory
  Aids in process understanding
  Avoids local optimization
  Improves communication between departments

## Slide 87: Evaluation of TOC
Disadvantages
  Negative impact on non-constrained areas
    Diverts attention from other areas that may be the next constraint
    Temptation to reduce capacity

## Slide 88: books

## Slide 89: What you should learn
Just-In-Time (JIT)
Value Stream Mapping (VSM) for lean manufacturing
Theory of Constraints (TOC)